Comparaison de differents softs pour la generation de MNT Pléaides.

Etapes du traitement.

- Pour chaque MNT Pléiades, ouverture du fichier geotif pour remplacer les « no_data » ou les « background_data » par des NaN. L’objectifs est d’éviter que ces no_data (par exemple -32767, -9999 ou -150 selon les softs) ne se propagent lors du ré-échantillonage. Un effet négatif de ce traitement est que les NaN « bavent » sur les pixels voisins...

- Initialement, on calcule aussi le % of data voids mais pour certains auteurs la valeur no_data et background est la même... les deux ne sont donc plus distinguables facilement. Le % of data gaps n'est donc calculé que pour la zone couverte par le lidar uniquement, dans le script suivant. Avec le défaut que le  resampling (cubic convolution) aura fortement augmenté leur % (comme expliqué ci-dessus).

- Stacking de chaque MNT Pléiades avec le MNT Lidar 4 m (ENVI > Basci Tools > Layer Stacking) avec un filtre de ré-échantillonage en cubic convolution. La zone commune est celle du LIDAR.

- Script IDL d’estimation du shift dans le MNT et, après correction du shift, des statistiques sur les différences d’altitude avec le MNT LIDAR. Les statistiques sont calculées en conservant toutes les valeurs (même clairement aberrantes) des MNTs. On a aussi établi des statistiques dans une gamme de valeur acceptable, par exemple [-20 m; 20 m] ou [-3*SD ; +3*SD].

- Script IDL pour comparer les MNT après 3D-coregistration à des données GPS acquises sur la calotte quelques jours avant l'acquisition Pléiades.

- Extraction des altitudes des différentes MNT le long de deux profils, l'un traversant la calotte et un autre sur les zones non (ou peu) englacées hors de la calotte.

- Dans les tableaux ci dessous, surligné en jaune les valeurs qui sortent du lot des 11 MNTs ce qui les rend suspect et en bleu les 2 ou 3 MNT qui ont les meilleurs résultats (plus faible dispersion)

- images d'ombrages (shaded relief) pour une zone au sud

356016	7183750

360670	7178970

Pb "techniques" rencontrés.

- MNT calculés sur seulement une partie de l'image

- Hauteurs non fournies par rapport à l'ellipsoid mais le geoid

Table 1: Software and the processing time to generate the 4-m DEM of Tungnafellsjökull

| Contact/Labo | Tool / soft | Open source (Y/N), if No cost of license | PC Configuration | Processing time |
| --- | --- | --- | --- | --- |
| Angelo DLR | XDibas/SGM | No (not distributed) | 8 core Xeon E5-2650 v2 @ 2.6 GHz, 64 bit Linux | 4h |
| Berthier LEGOS | PCI Geomatica 2013 / Orthoengine | No 4400 euros / 5 lic. 5300 eur / 10 lic. | OS: Windows 7 64 bits CPUs : 4 processeur: Intel Core CPU @ 3.4GHz RAM: 32 Go | 1h |
| deFranchis CMLA | s2p | Yes |  |  |
| Deloménie IGN Espace | Géométrie : outil IGN calgri Corrélation : MicMac | Non Oui | MacOS 10.8.5 Processeur : 2x2,66GHz 6 coeurs Intel Xeon RAM : 16Go 1333MHz DDR3 | 3h |
| Durand Sertit | Spatio maison / Mic Mac | Yes & No Spatio non Mic Mac oui |  |  |
| Ferry Geo Mptl | Erdas Imagine 2014, Toolbox Imagine Photogrammetry, Module eATE No TPs | No | OS: Windows 7 64 bits CPUs : processeur: Intel Xeon bi-processeur (20 coeurs) à 2.5 GHz RAM: 128 Go | 5h |
| Gascoin CESBIO | ERDAS eATE correl window: 15 on ice / 9 off + Gradient threshold ≠ on/off | No | OS: Windows 32 bits CPU: 1 Proc: Intel Core i5 @ 2.67 GHz RAM: 4 Go | 17h off glacier 9h on glacier |
| Girod Univ Oslo | Mic Mac only | Yes | RHEL6 CPU : 24 cores - 48 threads Proc : 2*Intel Xeon E5-2697v2 @ 2.7Ghz RAM : 192Go | Tie Points : 25min Spacio : 5min Correlation : 11min TOTAL : 40min |
| Guérin CEA | Euclidium + Mic Mac | Euclidium No Mic Mac Yes |  | 10h on personal (standard) laptop |
| Howat OSU | SETSM | Yes C binary and MATLAB versions freely available soon |  | 6h on a 4 CPUs PC |
| Lacroix ISTERRE | AMES Stereo pipeline (NASA) | Yes |  | 5h30 |
| Lucas GXP CEA (post doc CNES) | procédures personnelles sur SOCET GXP (BAE System) | No | OS: Windows 7 64 bits CPUs : processeur: Dual-Xeon RAM: 32 Go | 30h (tps CPU) |
| Magnusson/Belart Univ Iceland | ERDAS eATE (enhanced Automatic Terrain Extraction) | No | OS: CPUs : processeur: Intel Core i5-4670 CPU @ 3.40 GHz RAM: 8 Go | 1h15 |
| Rosu IPGP/IGN | Euclidium / Mic Mac | Euclidium No Mic Mac oui | OS: Ubuntu 64 bits CPUs : 4 processeur: Intel Xeon CPU E5630 @ 2.53GHz RAM: 6 Go | 7h for a full resolution DEM (0.55 m), then resampled at 4 m |
| Stumpf / Brest | Imagine photogrammetry | No | OS: Ubuntu 64 bits CPUs : 8 processeur: Intel XEON @ 2.3 Ghz RAM: | 9h |

Table 2: Evaluation of the 4-m Pleiades DEMs including the Tungnafelljökull Ice Cap (Iceland) against a Lidar DEM acquired 7-8 August 2011. The table provides the horizontal shifts of the Pleiades DEM and statistics (median, standard deviation and Normalized Median Absolute Deviation, NMAD Höhle & Höhle, 2009) of the elevation differences (dh, Pléiades – Lidar) outside the ice cap (stable terrain) after correcting for this horizontal shift. The last column indicates the average elevation differences on the ice cap between 7-8 August 2011 and 9 October 2013 after correcting the horizontal and vertical shifts. Sorted by alphabetical order. Note: Mean and Median are very similar for all DEMs. YELLOW= not so good. BLUE=Good. DEMs in italics (with gaps when a “no gap” exist with the same software) are not used to compute the median of all DEMs

| Soft | data gaps (%) | Shift East (m) | Shift North (m) | Median dh OFF (m) | Stddev dh OFF (m) | NMAD dh OFF (m) | Nb OFF | Mean dh ON (m) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Median Alls DSM |  | 2.12 | -1.24 | 3.27 | 1.22 | 0.74 |  | -1.56 |
| Angelo DLR No Gap | 0 | 1.98 | -1.11 | 3.37 | 0.85 | 0.64 | 3,411,658 | -1.58 |
| Berthier Geomatica | 0.4 | 2.12 | -1.29 | 3.66 | 1.72 | 0.74 | 3,381,501 | -1.58 |
| deFranchis s2p | 5.9 | 2.99 | -2.66 | 3.35 | 0.91 | 1.00 | 2,945,357 | 1.45 |
| Delomenie No Gap | 0 | 2.34 | -1.26 | 3.09 | 1.22 | 0.76 | 3,411,658 | -1.62 |
| Durand Mic Mac | 0 | 1.96 | -1.11 | 3.00 | 1.07 | 0.72 | 3,411,658 | -1.76 |
| Ferry ERDAS | 23.2 | 1.92 | 31.15 | -27.05 | 0.75 | 0.55 | 2,924,796 | -1.22 |
| Gascoin ERDAS | 0 | 1.87 | -0.86 | 3.74 | 1.75 | 0.63 | 3,411,658 | -1.54 |
| Girod Mic Mac STD | 0 | 2.05 | -1.40 | 2.27 | 1.89 | 1.48 | 3,411,658 | -1.69 |
| Guerin Mic Mac | 0 | 4.92 | -2.99 | 3.33 | 0.87 | 0.77 | 3,411,658 | -1.63 |
| Howat SETSM No Gap | 0 | 4.06 | -2.14 | 3.40 | 1.22 | 0.67 | 3,411,658 | -1.59 |
| Lacroix AMES | 0.6 | 2.50 | -1.24 | 3.36 | 1.13 | 1.03 | 3,359,469 | -1.56 |
| Lucas SOCET GXP | 2.8 | 9.16 | 14.85 | 0.63 | 2.28 | 1.40 | 3,411,658 | -1.43 |
| Magnusson ERDAS | 7.4 | 0.69 | 0.46 | 2.89 | 1.35 | 1.02 | 2,884,074 | -1.53 |
| Rosu Mic Mac | 0 | 3.04 | -1.29 | -3.35 | 0.89 | 0.68 | 3,411,658 | -1.53 |
| Stumpf IMAGINE | 0 | 2.05 | -0.97 | 3.27 | 1.53 | 0.71 | 3,411,658 | -1.54 |

Table 3: Same as Table 2 except that the statistics are computed after correcting the horizontal and vertical shift between the Pléiades DEM and the Lidar and ONLY over the 990,815 pixels for which a value is present in ALL DEMs. Mean and Median are not shown because, by construction, they are very close to zero for all DEMs (within a few centimeters for all DEMs). YELLOW= not so good. BLUE=Good

| Soft | Min_dh OFF (m) | Max_dh OFF (m) | Stddev_dh OFF (m) | NMAD_dh OFF (m) |
| --- | --- | --- | --- | --- |
| Median All DSM |  |  | 0.48 | 0.30 |
| Angelo DLR No Gap | -11 | 14 | 0.43 | 0.24 |
| Berthier Geomatica | -49 | 53 | 0.49 | 0.26 |
| deFranchis S2P | -83 | 15 | 0.80 | 0.48 |
| Delomenie No Gap | -65 | 19 | 0.48 | 0.30 |
| Durand Mic Mac | -11 | 13 | 0.44 | 0.28 |
| Ferry ERDAS | -71 | 14 | 0.47 | 0.22 |
| Gascoin ERDAS | -26 | 45 | 0.48 | 0.22 |
| Girod Mic Mac | -22 | 16 | 1.06 | 0.86 |
| Guerin Mic Mac | -11 | 13 | 0.47 | 0.32 |
| Howat SETSM No Gap | -11 | 13 | 0.42 | 0.27 |
| Lacroix AMES | -15 | 21 | 0.65 | 0.41 |
| Lucas SOCET GXP | -49 | 28 | 1.33 | 0.88 |
| Magnusson ERDAS | -99 | 16 | 0.70 | 0.45 |
| Rosu Mic Mac | -11 | 13 | 0.43 | 0.30 |
| Stumpf Imagine | -12 | 43 | 0.46 | 0.24 |

Table 4: Evaluation of the 4-m Pleiades DEMs with kinematic GPS measurements performed on/off the ice cap 18 September 2013, 21 days before the acquisition of the Pléiades images. Before comparison, all the Pléiades DEM have been horizontally and vertically registered to the Lidar DEM off glacier. Mean dh are not shown because they are very close to the median dh. YELLOW= not so good. BLUE=Good

| Soft | Median OFF ice (m) | Std dev OFF ice (m) | NMAD OFF ice (m) | Nb OFF | Median ON ice (m) | Std dev ON ice (m) | NMAD ON ice (m) | Nb ON |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Median All DSM | -0.08 | 0.71 | 0.39 |  | -0.05 | 0.37 | 0.29 |  |
| Angelo DLR | -0.08 | 0.65 | 0.35 | 1111 | -0.05 | 0.34 | 0.29 | 2754 |
| Berthier Geomatica | -0.11 | 1.57 | 0.36 | 1111 | -0.07 | 0.37 | 0.28 | 2754 |
| deFranchis s2p | -0.08 | 0.93 | 0.48 | 1009 | 0.01 | 0.41 | 0.30 | 2631 |
| Delomenie No Gap | -0.14 | 0.64 | 0.40 | 1111 | -0.08 | 0.38 | 0.34 | 2754 |
| Durand Mic Mac | -0.09 | 0.64 | 0.41 | 1111 | -0.19 | 0.37 | 0.32 | 2754 |
| Ferry ERDAS | -0.01 | 0.41 | 0.35 | 887 | 0.02 | 0.36 | 0.27 | 495 |
| Gascoin ERDAS | -0.07 | 1.20 | 0.37 | 1111 | -0.11 | 0.39 | 0.26 | 2754 |
| Girod Mic Mac | -0.06 | 1.88 | 0.72 | 1111 | -0.04 | 1.13 | 0.74 | 2754 |
| Guerin Mic Mac | -0.19 | 0.71 | 0.46 | 1111 | -0.15 | 0.52 | 0.44 | 2754 |
| Howat SETSM | -0.11 | 0.64 | 0.39 | 1111 | -0.10 | 0.40 | 0.34 | 2754 |
| Lacroix AMES | -0.08 | 0.61 | 0.38 | 1094 | -0.04 | 0.31 | 0.23 | 2753 |
| Lucas SOCET GXP | 0.20 | 0.94 | 0.71 | 1111 | 0.04 | 1.36 | 0.66 | 2754 |
| Magnusson ERDAS | -0.02 | 0.76 | 0.43 | 1020 | -0.01 | 0.28 | 0.24 | 2723 |
| Rosu Mic Mac | -0.03 | 0.56 | 0.34 | 1111 | 0.01 | 0.34 | 0.29 | 2754 |
| Stumpf Imagine | -0.09 | 1.19 | 0.37 | 1111 | -0.08 | 0.34 | 0.26 | 2754 |